## Slide 1: Delaware River Basin Commission
Recreational Uses & Criteria in the Delaware River
Delaware River Watershed Forum
October 16-17, 2019
Allentown, PA
John Yagecic, PE
Manager, Water Quality Assessment DRBC

## Slide 2: Delaware River Basin Commission
Compact signed 1961
Equal Members:
  Delaware
  New Jersey
  Pennsylvania
  New York
  Federal Government
Broad Responsibilities / Authorities
Water Supply
Drought Management
Flood Loss Reduction
Water Quality
  Establish Water Quality Standards
  Monitoring & Assessment
  Assimilative Capacity Determination
Watershed Planning
Regulatory Review (Permitting)
Outreach/Education
Recreation

## Slide 3: Water Quality Management Zones
WQM zone | Location (River Mile) | Tidal / Non-tidal
1A | 330.7 – 289.9 | Non-tidal
1B | 289.9 – 254.75 | Non-tidal
1C | 254.75 – 217.0 | Non-tidal
1D | 217.0 – 183.66 | Non-tidal
1E | 183.66 – 133.4 | Non-tidal
2 | 133.4 – 108.4 | Tidal
3 | 108.4 – 95.0 | Tidal
4 | 95.0 – 78.8 | Tidal
5 | 78.8 – 48.2 | Tidal
6 | 48.2 – 0.0 | Tidal

## Slide 4: Current Recreational Uses / Criteria in Delaware Estuary (DRBC WQ Regs)
Zone | Use | Fecal Coliform | Enterococcus
 |  | Geometric mean colonies per 100 mL | 
2 | Recreation | 200 | 33
3 | Recreation – Secondary Contact | 770 | 88
Upper 4 |  |  | 
Lower 4 | Recreation | 200 | 33
5 |  |  | 35
6 |  |  | 
http://www.nj.gov/drbc/library/documents/WQregs.pdf

## Slide 5: DRBC Water Quality Regulations Section 1.20.6
http://www.nj.gov/drbc/library/documents/WQregs.pdf

## Slide 6: EPA Office of Water 820-F-12-058
https://www.epa.gov/sites/production/files/2015-10/documents/rwqc2012.pdf

## Slide 7: 1988 Attainability Report

## Slide 8: Combined Sewer Overflows
Sanitary sewage and storm water in same pipes
When flow exceeds capacity, overflows without treatment
Legacy systems (100+ years) in our oldest, largest communities
Image credit: Jersey Water Works

## Slide 9: What has Changed since 1988?
CSO Long Term control programs are in place, making progress
Much more accurate models of CSO systems – volume and timing of discharge
Effort & enthusiasm for reconnecting regional urban areas to their waterways
Very high level of public / NGO interest in this issue
Statistical models providing guidance on current conditions relevant to contact recreation

## Slide 10: CSO Long Term Control Plans

## Slide 11: PWD’s Green City, Clean Waters Project by Project
Some completed projects
Some future projects
From PWD’s 2018 CSO & MS4 annual report at:
http://archive.phillywatersheds.org/what_were_doing/documents_and_data/CSO_SW_AnnualReports

## Slide 12: Uses Happening Now
Photo credit: Paul Michael Bergeron
Photo credit: Aqua Vida
Photo credit: Aqua Vida

## Slide 13: Gradient of Primary Contact Criteria Attainment
Primary contact criteria
never met
Primary contact criteria
always met
Where are
we now?

## Slide 14: DRBC Monitoring
DRBC’s long-running (50+ year) monitoring program
1x per month
Center channel
Just below Trenton to just above Atlantic Ocean
Bacteria results posted on DRBC web site at https://www.nj.gov/drbc/quality/datum/boat-run.html

## Slide 15: Monitoring Summer 2019
Shore-based, where recreation more likely
~ 5x per month, May - September
Fecal coliform, enterococcus, E. coli
Riverton Yacht Club
Palmyra Cove Nature Center
Pennsauken Access
Pyne Poynt Park
National Park
Washington Ave. Green
Penns Landing Lagoon
Frankford Arsenal Boat Ramp
NJ
PA

## Slide 16
http://www.phillyrivercast.org/

## Slide 17: DRBC Next Steps
Assess the shore-based data collected in 2019
Boat-based transect monitoring in 2020 to determine if near-shore concentrations are higher than center channel concentrations
Coordination with our Water Quality Advisory Committee (WQAC)
https://www.nj.gov/drbc/about/advisory/WQAC_index.html

## Slide 18: Other Hazards / Other Challenges
Busy shipping ports
Hazardous currents
Debris, pilings, junk
Beaches have an elaborate protocol for monitoring, beach closures, re-opening
Liability >> Responsibility & Authority

## Slide 19: What can you do?
Citizens
Stay tuned in to DRBC’s Water Quality Advisory Committee & list servs
Volunteer monitoring? Maybe, but…
  Develop & follow an approved Quality Assurance Project Plan (QAPP)
  State certified laboratory
  Short 6-hour holding time from sample dip to drop off at lab
  Get your data into WQX
  Government organizations cannot take on liability for volunteers
NGOs
Support development of forecasting tool
Support monitoring
Support green infrastructure?

## Slide 20: Questions & Discussion
Resources
DRBC’s Water Quality Advisory Committee
https://www.nj.gov/drbc/about/advisory/WQAC_index.html
DRBC e-mail groups
https://www.nj.gov/drbc/contact/interest/index.html
Philadelphia Green City Clean Waters
https://www.phila.gov/water/sustainability/greencitycleanwaters/Pages/default.aspx
Camden County MUA Green Infrastructure
http://www.ccmua.org/index.php/green-initiatives/green-infrastructure/
Contact
John Yagecic
John.Yagecic@drbc.gov
609-883-9500 x271